## Slide 1: Improving Performance using the LINUX IO Scheduler
Shaun de Witt
STFC
ISGC2016

## Slide 2: Role of the Scheduler
Optimise Access to Storage
  CPU operations have a few processor cycles (each cycle is < 1ns)
  Seek operations take about ~> 8ms (25 million times longer)
Reorder IO requests to minimise seek time
Two main operations – sorting and merging
  Sorting arranges block reads sequentially
  Merging makes two adjacent block reads into one

## Slide 3: Where the Scheduler Sits
© Werner Fischer & Georg Schonberger
https://www.thomas-krenn.com/en/wiki/Linux_Storage_Stack_Diagram

## Slide 4: Available Schedulers
Linux Kernel >= 2.4 has 4 schedulers
  CFQ (default)
  Deadline
  Anticipatory
  Noop

## Slide 5: Completely Fair Queueing
Each IO device gets its own queue and each queue gets its own timeslice
Scheduler reads each queue in round-robin until end of timeslice
Reads prioritised over writes

## Slide 6: Deadline
Three queues
  Elevator queue containing all sorted read requests
  Read-FIFO queue containing time ordered read requests
  Write-FIFO queue containing time ordered write requests
Each request in FIFO queue has an ‘expiration time’ of 500 ms
Normally requests are served from the elevator queue, but as requests expire in the FIFO queue, these queues will take precedence
Gives good avaerage latency but can reduce global throughput

## Slide 7: Anticipatory
Similar to deadline scheduler
  But with some anticipatory knowledge – expectation of a subsequent read
Read requests serviced within deadline, but then pauses for 6ms, waiting for a subsequent read of the next block
In general, this works well if most reads are dependent (e.g. reading sequential blocks in a streaming operation)
  But may be poor for vector reads

## Slide 8: NOOP
Simplest scheduler
Only does basic merging
  NO SORTING
Recommended for non-seeking devices (e.g. SSDs)

## Slide 9: Hardware Set-up at RAL
Diskservers configured in RAID6 or RAID60 with 3 partitions
  Allows for two independent disk failures without losing data
Uses hardware RAID controllers
  Various vendors dependent on procurement
Unusual Horizontal striping
  Minimise RAID storage overhead

## Slide 10: RAID Configuration
FS1
FS2
FS3
‘Typical’ RAID6
Configuration
RAL RAID6 Configuration

## Slide 11: Impact of Using Hardware RAID
RAID controller has fairly big cache
  Able to write quickly for large periods of time
But now CFQ sees only one device (or one for each filesystem)
Scheduler sorts iops assuming a well defined disk layout
  But RAID controller has a different layout and will resort it
Not normally a significant overhead, until the iops become large and effectively random
  Double sorting and different cache sizes between kernel and RAID controller lead to massive inefficiencies
  Almost all application time spent in WIO

## Slide 12: What made RAL look at this

## Slide 13: CMS Problems
Accessing disk-only storage under LHC Run 2 Load
All disk servers (~20) running at 100% WIO
  Only certain workflows (pileup)
  Job efficiencies running <30%
  Other Tier 1 sites also had problems, but were much better (~60% CPU efficiency)
  ‘Normal’ CPU efficiencies run >95%

## Slide 14: Solutions…
Limit number of transfers to each disk server
  Jobs timeout waiting for storage system scheduling
  Means few jobs run well, but most fail
Limit number of pileup jobs on the processing farm
  No reliable mechanism for identifying them
Add more disk servers
  Would work, but would have cost implications

## Slide 15: Finally…
Try switching scheduler…
  Can be done and reverted ‘on the fly’
    Does not require a reboot
  Can be applied on a single server to investigate the impact
Preemptive CAVEAT
  Don’t try this at home!
  Software RAID and different RAID controllers will behave differently
  Only do this if either
    Your storage system is already ‘overloaded’
    You have tested the impact with your hardware configuration

## Slide 16: Anecdotal Impact
Switched to NOOP scheduler
  WIO reduced from 100% to 65%
  Throughput increased from 50Mb/s to 200Mb/s
Based on making a change to 1 server under production workload

## Slide 17: Anecdotal Impact

## Slide 18: Anecdotal Impact

## Slide 19: Attempt to Quantify
Heavy WIO reproduced by
  Multiple jobs reading/writing whole files (1GB random data)
  Different R/W mixing
  Using xrootd protocol
200 different files for reading (try to remove any effect of caching reads)

## Slide 20: 50-50 Job Mix
Chart: 50-50 Job Mix, READ rates
| 10.0 | 25.0 | 50.0 | 100.0 | 150.0 | 200.0
CFQ | 0 | 26.2453 | 24.7181 | 111.8967 | 21.4178 | 20.5968
NOOP | 34.0212 | 61.3257 | 73.0618 | 78.2473 | 225.9176 | 213.7433
Chart: 50-50 Job Mix, WRITE rates
| 10.0 | 25.0 | 50.0 | 100.0 | 150.0 | 200.0
CFQ | 0 | 140.413 | 367.2151 | 592.4758 | 1011.0205 | 825.1285
NOOP | 24.3647 | 69.119 | 203.6872 | 641.5813 | 801.4389 | 901.7673

## Slide 21
50-50 Job Mix (100 jobs)
CFQ
NOOP

## Slide 22: Read Dominated (80-20) Job Mix
Chart: 80-20 Job Mix, READ rates
| 10.0 | 25.0 | 50.0 | 100.0 | 150.0 | 200.0
CFQ | 34.7592 | 31.1372 | 31.154 | 26.2399 | 31.325 | 33.4751
NOOP | 34.0212 | 61.3257 | 73.0618 | 78.2473 | 225.9176 | 213.7433
Chart: 80-20 Job Mix, WRITE rates
| 10.0 | 25.0 | 50.0 | 100.0 | 150.0 | 200.0
CFQ | 108.919 | 220.5317 | 582.4742 | 768.4366 | 1014.7993 | 887.6681
NOOP | 41.1145 | 96.4832 | 62.2052 | 248.5615 | 534.9027 | 1064.8388

## Slide 23
Read Dominated Job Mix
CFQ
NOOP

## Slide 24: Write-Dominated (20-80) Job Mix
Chart: 20-80 Job Mix, READ rates
| 10.0 | 25.0 | 50.0 | 100.0 | 150.0 | 200.0
CFQ | 40.971 | 24.086 | 23.4117 | 27.6159 | 26.5415 | 23.0925
NOOP | 29.6254 | 35.3059 | 43.2045 | 31.6066 | 39.2325 | 45.4394
Chart: 20-80 Job Mix, WRITE rates
| 10.0 | 25.0 | 50.0 | 100.0 | 150.0 | 200.0
CFQ | 49.9667 | 112.503 | 220.8481 | 474.075 | 743.8861 | 801.1156
NOOP | 41.1145 | 96.4832 | 62.2052 | 248.5615 | 534.9027 | 1064.8388

## Slide 25
Read Dominated Job Mix
CFQ
NOOP

## Slide 26: Summary & Conclusion
Attempted controlled tests showed no significant benefit of using NOOP or CFQ schedulers
  ATLAS problems bear this out
… or to spin results positively
  There is no detriment observed to using NOOP over CFQ
Left with the question what is it about the pile-up jobs that causes such a bad impact on the disk servers, and why does NOOP give such a big gain
Questions – Because I still have many!