## Slide 1: A Study of Certification Authority Integration Model in a PKI Trust Federation on Distributed Infrastructures for Academic Research
Eisaku SAKANE, Takeshi NISHIMURA, Kento AIDA
National Institute of Informatics, Japan
International Symposium on Grids & Clouds 2016
15 March 2016
Academia Sinica, Taipei, Taiwan

## Slide 2: Outline
Introduction
Objects and Issues
  Typical CA Architecture
Proposals
Discussions
Related Works
Summary

## Slide 3: Introduction
Background
  Among certification authorities (CAs) in an academic PKI trust federation, most of academic organizations that operate CA install by themselves the CA equipment in their building.
  It is necessary to maintain such CA equipment and to obtain the special operators.
  Consequently, the high cost of CA operation weighs heavily on the CA organization.
  For research institutes whose essential duties are not the CA operation, the burden on the high cost of CA operation is an earnest problem, and cost reduction with increasing the efficiency of the operation is an important issue.

## Slide 4: Introduction (cont’d)
Guiding question
  How about trying for more than one operating organization to reduce cost operations?
Importance of the research
  We propose a method of increasing the efficiency of CA operations in cooperation between more than one CA operating organization.

## Slide 5: Premise of the Argument
We do not discuss how to build from scratch a CA that covers each research community.
  Keep the independence of CA operating organization.
We do not discuss the following:
  Two CA operating organizations outsource CA to a commercial CA vendor and share the expenses.
We discuss how to integrate existing CAs without being forced to a drastic change in order to reduce the cost of the CA operations.
  From user’s point of view, CA service procedures for users should be unchanged as possible.
  From operator’s point of view, the changes of CA operation procedures should be small if possible.

## Slide 6: Typical CA Architecture
CA architecture in question
  Composed of IA and RA servers
  IA located in a private network connects only the RA and is a dedicate machine for only signing operations.
  RA connected to the public network receives the request from end-entities and conveys it to the IA.
Certificate Policy A
IA
RA
End entities, Relying parties
HSM

## Slide 7: Typical CA Architecture (cont’d)
Certificate Policy B
IA
RA
End entities,
Relying parties
Certificate Policy A
IA
RA
End entities, Relying parties
HSM
HSM

## Slide 8: Basic Idea
Interference in certificate policies would be kept down to a minimum if each RA is independently operated as before.
  The research community should have the responsibility to vet user identities.
  It is difficult for one RA to vet user identities in the other community because RA operations are heavy duties.
Issuing operations are the following:
  Strictly management of the CA private key
  Response to the requests from the RA
It would be unnecessary to operate the IA at one’s own expense as long as the IA communicates reliable RAs.
The integration of IAs is more better.

## Slide 9: How to connect RA with outside IA
Certificate Policy B
RA(β)
End entities,
Relying parties
Certificate Policy A
IA
RA
End entities, Relying parties
HSM
How connect?

## Slide 10: Proposed IA-RA Connections
Direct connection
  A virtual private network (VPN) connecting between RA(β) and IA.
Relaying RA
  Secure connection IA-RA-RA(β) on the public network.

## Slide 11: Direct Connecting: VPN
Certificate Policy A
Certificate Policy B
Internet
IA
RA
End entities
RA(β)
End Entities
VPN
HSM

## Slide 12: Relaying RA
Certificate Policy A
Certificate Policy B
Internet
IA
RA
End entities
RA(β)
End Entities
HSM

## Slide 13: Relaying RA (cont’d)
Certificate Policy A
IAd
RAd
Clients
Certificate Policy B
RAd(β)
Clients
RAd-compat.
Secure connection
Sending a request to “IA” as before
Receiving the request like “IA”
HSM

## Slide 14: Discussion on IA-RA connection
Direct connecting
  Advantages
    Unchanged I/F to users.
    Basically no software development.
  Disadvantages
    Some trouble to establish a VPN.
    Further difficulty in connecting CA components across countries via VPN
Relaying RA
  Advantages
    Unchanged I/F to users.
    No difficulty with network infrastructure.
  Disadvantages
    Software development is needed.
    Connection depends on the software package.

## Slide 15: Discussion on AP
There are two CA authentication profiles that enable CA to issue long-lived certificates, provided by IGTF:
  Classic
  MICS (Member Integrated Credential Service)
An example of 4 combinations
  IA and RA: MICS, RA(β): Classic
  RA(β) should change from Classic RA to MICS IdM.
  This basically ensure each independence of organization and does not interfere in the policy.
  IA needs to go through the formalities for permit it to issue certificates to the RA(β).

## Slide 16: Related Works
RPS (Registration Practice Statement)
  Discussed in IGTF
  Can be considered as a subordinate document to the CPS
  It is suggested that separating RAs from the CA function has benefits that are useful for more efficient trust processing of the overall system.
  RPS framework would help the proposed integration model in policy arrangement.
ASGC CA as real integrated CA
  ASGC CA has foreign RAs such as AU, NZ, VN, PH.

## Slide 17: Summary
We considered an integration model of certificate authorities in a PKI trust federation such IGTF.
We proposed two connection types between IA and RA:
  Direct connecting using VPN
  Relaying RA
We would like to implement the proposed relaying RA model to NAREGI-CA software and perform demonstrative evaluation.
We would like to consider integration procedures with RPS framework.