## Slide 2: Design and implementation of the IO Framework for HEPS
Speaker: Fu Shiyuan
IHEP computing center, postdoctoral
<fusy@ihep.ac.cn>

## Slide 3: Outlines
Introduction
Unified I/O interface
Optimization for batch processing
Stream processing
Conclusion

## Slide 4: Introduction for HEPS
HEPS：High Energy Photon Source
  Include multi beamline
HEPS will generate a huge mount of data
  In which the data volume generated by B7 is the most
The huge mount of data will give great pressure to storage and computing
Chart: beamline
| B1 | B2 | B3 | B4 | B5 | B6 | B7 | B8 | B9 | BA | BB | BC | BD | BE | BF
Mean Data Volume Per Day (TB) | 200 | 200 | 3 | 3 | 1 | 1 | 250 | 10 | 5 | 10 | 50 | 0.2 | 1 | 11.2 | 60

## Slide 5: Introduction for HEPS
Design and implement HEPS I/O optimization methods, and integrate them with Daisy[1].
  To address the diverse applications of HEPS, shield the differences in underlying data (source, format) → unify the I/O interface
  Alleviate the severe IO bottleneck issues in HEPS-related applications and accelerate scientific processing → batch IO acceleration
  Avoid I/O bottlenecks caused by data writing and reading on disk→ stream processing I/O support.
DAQ
Storage
Stream Processing
Batch Processing
IO Interface
1
2
3
[1]“Recent developments in the data analysis integrated software system of HEPS”
"VRE”thesession, 14:0015:30,Tuesday,26 March.

## Slide 6: Daisy I/O method
  Background:
    Belongs to the DataHandlerAlg module of Daisy
    Includes various formats of Load and Save methods
    Selects Load and Save methods through configuration
  Issues:
    Inconsistent parameters for different format methods, not user-friendly
    Lack of support for distributed computing and stream processing
  Goal:
    Design and implement unified, distributed I/O methods that shield differences in underlying data sources, data formats, application I/O method libraries, and computational parallelism.
Daisy.DataHdlerAlg
  LoadHdf5
  LoadTiff
  LoadHdf5master
  SaveHdf5
  SaveTiff
  SaveHdf5Master

## Slide 7: Daisy Unified I/O
A. Design and implement Daisy DataHandlerAlg
B. Design and implement a unified I/O interface.
  Research the different applications’ requirements for I/O.
  Standardizing different sources (DISK, STREAM) and different applications (XAS, pychophy) through configuration (cfg).
  Automatically determining file formats (TIFF, HDF5, Dat).
C. Supporting parallel computing.
Daisy.DataHdlerAlg
  LoadHdf5
  LoadTiff
  LoadHdf5master
  SaveHdf5
  SaveTiff
  SaveHdf5Master
Daisy.DataHdlerAlg
  LoadData
  SaveData
  Utils
    hdf5.py
    tiff.py
    xas.py
    stream.py
Cfg Dict
Type：DISK/STREAM
Input_file: input file path
Beamtime_id
Source_ip
Alg: XAS etc.
……
Format
Algs
Stream
Computing task
Unified IO Interface
writer
reader
initialize
conf
execute
Parse cfg and set the relevant parameters.
Initialization, setting the degree of parallelism for computation.
Read the actual data required for the process and store it in the DataStore.

## Slide 8: Speedup batch processing
Batch processing I/O optimization for computational acceleration
  optimizing for different data formats
    HDF5 master parallel prefetch strategy
    HDF5 direct I/O
    multi-threading acceleration for TIFF
  Specific applications benefit from I/O optimization
    asynchronous I/O for HEPSCT (increased by 25%).
0001
0002
0003
0001.h5
0002.h5
0003.h5
master.h5
1
ReadTiff.h
ReadTiff.cpp
ReadTiff.pxd
ReadTiff.pyx
ReadTiff.so
ReadTiff.py
Implementing multithreading in C++.
Using Cython to call C++ function
Compile a .so file for use in Python.
Using Python to call the .so file and read TIFF data with multiple threads.
3
read
Preprocess
reconstruction
postprocess
write
4
2
Chart: hdf5 read time/s
| driect io without format convert | direct io with format convert | direct io with memory copy | originnal
read | 14 | 14 | 14 | 14
memory copy | 0 | 0 | 4 | 0
data append | 0 | 0 | 0 | 8
format convert | 0 | 5 | 4 | 4

## Slide 9: Daisy Stream I/O
Background:
  Data is processed after being written to disk.
Issues:
  IO bottlenecks may significantly impact the efficiency of scientific computing.
  There is a need for quick visualization of small amounts data.
Goal:
  To avoid IO bottlenecks caused by writing data to disk and then reading it by implementing a data streaming approach.
Methods:
  Design and implement the streaming data processing
  Define data stream interface parameters
  Develop the unified modules for streaming data access, parsing, management, and retrieval.
DAQ
Storage
Batch process
IO Interface
DAQ
Storage
StreamProcess
BatchProcess
IO Interface
Distributed Memory

## Slide 10: Daisy Stream I/O
To meet the needs of HEPS, a streaming data processing based on Flink and Alluxio has been designed.
  Flink is responsible for receiving data streams from different DAQ systems, parsing arrays, assembling, and performing some simple processing.
  Alluxio is responsible for temporarily storing the data processed by Flink for access by the computing platform.
DAQ A
json
dict
result
json
dict
result
Stream-process Job A
Stream-process Job B
Stream-process Job C
DAQ B
DAQ C
1.dat
all.dat
1.dat
2.dat
Path_A
Path_B
Path_C
Daisy IO
Daisy computing engine
Consistency with the Daisy IO method
Additional stream processing parameters

## Slide 11: Daisy Stream I/O
Develop a unified module for streaming data access, parsing, management, and retrieval.
  Access: Receiving data streams from the DAQ
  Parsing: Parsing the data stream into a dictionary format
  Management: Defining the data storage path
  Retrieval: Providing functionality for data retrieval and metadata listing
  Clarify the rules for integrating the new stream processing.
DAQ
DataRec
A data access API designed for computational tasks.
Buidl path based on beamlineName/
Beamtimeid…
Parsing streaming data based on different beamline configurations.
Building multiple stream data access based on ZeroMQ.
DataRec
DataRec
DataPrase
config
/path/A.dat
/path/B.dat
Read()
ls()
Stream Processing
Design the Daisy streaming data structure
Establish mapping relationships with the DAQ streaming data structure
Automate parsing of streaming data from different beamlines
Minimize the impact of changes in the streaming data structure on code maintenance as much as possible

## Slide 12: Conclusion
Provide a unified I/O interface to the computation, effectively shielding the underlying data format differences
Speedup batch process by parallelizing/prefetching/asynchronously
Use stream data I/O to avoid the I/O bottleneck and support online processing
DAQ
Storage
Stream Processing
Batch Processing
IO Interface
1
2
3
Thanks for your attention!
Q&A