## Slide 1: Experiences of hard disk management in an erasure coded 10 petabyte-scale Ceph cluster
Rob Appleyard, Tom Byrne

## Slide 2: Ceph at RAL
The STFC Rutherford Appleton Laboratory hosts the UK's WLCG Tier 1 Centre
  Data storage on disk & tape
  Large batch processing farm
  Tier 1 for ATLAS, CMS, LHCb, and ALICE
We use Ceph for two main applications:
  Backend storage for private cloud ('Sirius')
  Large erasure-coded storage service for WLCG disk storage ('Echo')
This talk will discuss Echo

## Slide 3: Previous talks
ISGC 2014 – First Experiences with Ceph on the WLCG
  http://indico3.twgrid.org/indico/contributionDisplay.py?sessionId=29&contribId=132&confId=513
HEPiX Spring 2015 - Ceph storage at RAL
  https://indico.cern.ch/event/346931/contributions/817835/
HEPiX Fall 2015 – Ceph object storage at RAL
  https://indico.cern.ch/event/384358/contributions/909231/
HEPiX Spring 2016 – Why so Sirius? Ceph backed storage at the RAL Tier-1
  https://indico.cern.ch/event/466991/contributions/2136880/
CHEP 2016 – The deployment of a large scale object store at the RAL Tier-1
  https://indico.cern.ch/event/505613/contributions/2230932/
Regular presentations at HEP Ceph meetings:
  https://indico.cern.ch/category/4866/

## Slide 4: Talk Structure
Part 1: Echo – A large scale, erasure coded, Ceph storage service
Part 2: Managing disk errors in a 10PB object store

## Slide 5: Echo – A large scale, erasure coded, Ceph storage service
Part 1

## Slide 6: Project startup
The story of Echo
  2014: CASTOR system (developed at CERN) providing both 'disk-only' and 'tape-backed' storage.
    CASTOR is very good at tape-backed storage, but not so good at disk-only.
    CERN's implementation of disk-only CASTOR retired
CASTOR uses a large Oracle DB for metadata and 130 ~100TB RAID 6 storage nodes
New system required to replace CASTOR disk-only

## Slide 7: Project Objectives/Requirements
We needed a service that satisfied these requirements*:
  MUST support WLCG-specific protocols (xrootd, gridftp), while also being able to support non-HEP use cases
  MUST scale well past 20PB usable space
  MUST cost no more in terms of £/TB than CASTOR, either in terms of hardware or staff effort
*Requirement keywords should be interpreted based on RFC2119

## Slide 8: Project Objectives/Requirements
Other desirable features of solution*:
  SHOULD have a broad support community
  SHOULD NOT be dependent on a restrictively-licensed third-party product (even if the product itself is licensed)
  SHOULD be resilient to hardware failure, on the level of disk, node and memory.
*Requirement keywords should be interpreted based on RFC2119

## Slide 9: Echo
Ceph evaluated as the best available solution
  But implemented in a specific way.
  See my talk from 2014 for more details!*
Erasure-Coded, High-throughput Object store
Key design choices:
  8+3 Erasure-coding:
    Better ratio of raw/usable space than replication
    Better data security than dual-replication
    …but more complicated
  Access method
    CephFS/similar not sufficiently mature and concerns over scalability*
    Needed to provide WLCG with access via Xrootd and GridFTP protocols
      Not feasible for VOs to simply use radosgw (S3) immediately
      So we need to have a translation layer to support these protocols
  * At the time that the decision was taken – see 2014 ISGC talk
Notes: ‘Echtos’ would be a much worse name

## Slide 10: How we provide access to Echo
‘Gateways’
Ceph Cluster
globus-gridftp-server
radosgw
xrootd
rados plugin
rados plugin
wLCG VO
Data Systems
FTS3
New VO
Services
S3
S3
gsiftp
gsiftp
VO data pool
RADOS
RADOS
xroot
rgw pool
libradosstriper
libradosstriper

## Slide 11: Gateways (1)
Gateways cache between external clients and Ceph storage
Need to be simple, lightweight
  WLCG VOs largely treat CASTOR largely as a simple object store, so give them that
Gateway systems need to have control over how the data is written
  Future proofing
  Users need XrootD and GridFTP need to be able to read data written by the other protocol
Solution: communicate at the RADOS object store level
  Use libRadosStriper to do this.

## Slide 12: Gateways (2)
All in/outbound data flows through a gateway system
  Obvious bottleneck
For external transfers, we have 5 dedicated gateway nodes
For transfers to local batch farm, every worker node hosts a gateway
  Maximises parallel access to system
  Works very well
New concept to run at RAL
  CASTOR equivalent system supplies address of correct storage node to protocol, no data passes through

## Slide 13: libRadosStriper
Library that provides an interface to Ceph’s low-level object store
Split large, incoming files into 64MB Ceph objects
  When a file is read, fetch required stripes, reassemble them on the gateway, serve to client.
Stripes data into Ceph using librados
  libRadosStriper integrated into official Ceph build as of Hammer
  Any plugin that uses it can read data written by any other plugin that uses it

## Slide 14: XrootD
XrootD plugin was developed by CERN using libRadosStriper
  Plugin is part of XRootD server software
  CERN use case is very restricted
  They switched from EC back to using replication.
We have a more complex setup.
  Direct I/O on EC pools was predictably slow.
    Implemented disk/memory caching on the gateways.
We have encountered many bugs that have been fixed
  Issues with checksumming, redirection and the caching proxy

## Slide 15: GridFTP
Plugin stable since October 2016
  Initial work by Sébastien Ponce (CERN) in 2015, based on XrootD plugin
    …so it also uses libRadosStriper
  Completed by Ian Johnson (STFC)
Same interface to RADOS as the XrootD plugin
  …so cross-reading with GridFTP works fine.
  https://github.com/stfc/gridFTPCephPlugin
Authentication/authorisation use the same software as xrootd

## Slide 16: Echo Architecture
WN
Ceph Cluster
VO data pool
Worker Node
XRootD server
rados plugin
libradosstriper
GW container
XRootD client
User job
Job container
XRootD client
User job
XRootD client
User job
Job container
Job container
Job
Job
Job
Job
Job
GW
WN
Job
Job
Job
Job
Job
GW
WN
Job
Job
Job
Job
Job
GW
WN
Job
Job
Job
Job
Job
GW
GridFTP server
rados plugin
libradosstriper
External GW
GridFTP server
rados plugin
Other sites
libradosstriper
External GW

## Slide 17: Erasure Coding (1)
Erasure coding is the technology that underlies non-replicated RAID (RAID 5/6)
  Split file into m pieces, write m+k pieces
  Object can be re-created from any set of m pieces
The erasure coding scheme for our main data store is 8+3:
  m=8, k=3
  8 data stripes
  3 parity stripes
On each write:
  For each 64MB stripe, split it into 8 data stripes, generate 3 parity stripes

## Slide 18: Erasure Coding (2)
Both m and k are tuneable
  Ratio and sum are both relevant
  High total number of stripes – smaller parity stripes
    …but also increased computational complexity of synchronisation operations
  Low m/k ratio: Greater data security
    …but also lower ratio of raw:usable storage
8+3 is the final compromise
  It’s also what we know that another user (Yahoo) does ;)
  Synchronisation is still computationally nontrivial

## Slide 19: Current Status
ATLAS - full production for workflows at RAL
  Steady migration of data from CASTOR system
CMS - in early stages of using Echo in production
  Starting to ramp up data volume and transfer rates
LHCb - still on CASTOR
  Work ongoing
  Hope to complete migration by Q4 2018
ALICE – also still on CASTOR
  Currently not migrating
  CASTOR disk-only data volume is only 500TB
Objective: No CASTOR disk-only data by April 2019

## Slide 20: Data Throughput
CASTOR:
Echo:
Notes: Just picked a random day for CASTOR

## Slide 21: Part 2: Managing disk errors in a 10PB object store
Part 2

## Slide 22: Reference for non-Ceph people
‘Object Storage Daemon’ (OSD)
  The daemon that manages an individual hard disk (1:1)
  Many OSDs per storage node
‘Placement group’ (PG)
  A subset of all our OSDs that form an 8+3 erasure coded set

## Slide 23: Disk management problems
Echo HW: large (200TB) storage nodes
  One OSD per disk
  13 PB raw (11 usable), 6TB/disk, 2160 total hard disks
  At this scale, disk errors are inevitable and routine
No RAID card
This means that disk errors that would be handled by RAID, are not.
Bad sectors visible to Ceph
  Ceph encounters read errors, has to handle them
  New problem for RAL (CASTOR storage nodes have RAID cards)

## Slide 24: Scrubbing & Data Integrity Checking
Ceph performs routine ‘scrubbing’ operations automatically to check data integrity
  Scrubbing: for a given placement group, read every object and validate
  If we get a read error, raise alarm
Necessary to catch bad sectors on disks

## Slide 25: What happens when Ceph encounters a bad sector?
Read error is passed to Ceph from the operating system
If the read error is encountered during a transfer...
  Not a problem for EC pools: Gateway requests all 11 shards, and uses the first 8 shards that don't return errors.
  Does not cause a HEALTH_ERROR state.
If the read error is encountered during scrubbing
  'Scrub error'
  Placement group is marked as inconsistent
  Results in a HEALTH_ERROR state on the cluster
  Most serious state that Ceph can report
    …but the fix is just to run ceph pg repair and all is OK again

## Slide 26: Aside: Why treat an inconsistent PG so seriously?
Ceph isn't designed for things to change on disk
  It's good at dealing with 'hard' failures
    Lose entire disk
    Lose entire server
    Lose entire rack
For replicated pools (most common configuration)
  Data changing on disk is dangerous
    All is fine if we have 2 matching copies left (they are probably correct)
    If we don’t, PG is inconsistent – may need human intervention - alarm
Not such a problem in EC land
  We can easily figure out which version is correct because of the 3 parity shards
  Ideally, Ceph should understand this.

## Slide 27: What does this mean operationally?
HEALTH_ERROR is potentially very serious
  Could be loss of availability, loss of data, cluster down
  Must callout 24/7, even if it's probably a scrubbing error causing a PG to go inconsistent
  Cluster frequently going into this state can mask more serious problems
    Very serious problem: Kraken 'EC Backfill' bug caused major data loss (23k files)
A cluster the size of Echo (~2000 OSDs) will encounter pending sectors
  Statistically inevitable

## Slide 28: What are we doing about it? (1)
Disks with pending sectors (from read errors, not scrubbing) need to be removed – if possible, preemptively
  Before the scrubbing finds the problem and causes a callout
  Use smartctl to monitor disks, send alert to Nagios
Use ceph.conf setting to prevent scrubbing from running overnight
PG scrub frequency reduced from default (1 week) to 1 month
  Scrubbing all PGs takes over a week…

## Slide 29: What are we doing about it? (2)
Mismatch between what Ceph ‘sees’ as a broken disk and what manufacturers will accept as a broken disk
  We can't just return a disk to the vendor whenever it gets a single pending sector
  This is NOT a ‘broken’ disk
Need to deal with low numbers of pending sectors internally
  If we leave a failing disk in Ceph it will accumulate errors and keep causing trouble (whenever it scrubs)
  Not acceptable operationally
Project to develop in-house tools to recycle a 'bad' (but not that bad) disk back into service

## Slide 30: Recycling Tools
Planned workflow:
  We write to every sector on the disk...
    existing pending sectors will be remapped if necessary
  ...and then read them all.
    new bad sectors, if any exist, will be discovered
If this operation completes without any errors, the disk can now be treated as good and returned to cluster
  If it fails, it will typically have recorded enough errors for return to manufacturer
Process to do this automatically under development at RAL
  Management process, not programming problem
  This is a stopgap – long term solution is for Ceph to handle this better.

## Slide 31: Where do we go in the future?
Previous system (CASTOR) had clear delineation between service admin and fabric admin
  RAID cards could protect storage system from disk errors
  Team very accustomed to this way of working
Not true for Ceph – hardware directly exposed to storage system
Problem manifests on Ceph side, initial responsibility goes to Ceph team
Need to develop new procedures to allow hardware team to intervene without the assistance of storage admins
  New staff member to develop processes

## Slide 32: Conclusion
STFC have built a Ceph-based storage system that is working well
  Large data volume
  Large throughput
Big throughput increase
WLCG VOs busy migrating from CASTOR
Some issues with disk management
  But we are working to mitigate them

## Slide 33: Any Questions?
Image from Hubble Space Telescope, owned by NASA, marked for non-commercial reuse https://www.nasa.gov/mission_pages/hubble/news/arp_194.html

## Slide 34: Spare slides
Appendix

## Slide 35: Aside: How Hard Disks deal with bad sectors
Sector: 512- or 4096- byte subdivision on a hard drive. Smallest unit of storage on the HD
Timeline:
  Sector fails to read
  HD returns a read error to the accessing process via the OS
  We now have a 'pending sector' (pending remap) - data from sector may be gone
  This state can end if we try to read again and it works, or...
  At some point, something will try to overwrite this sector
  Either overwrite is successful (transient problem affecting data not underlying structure)
  Or it isn't – sector is 'remapped' to a spare sector set aside for this purpose
    Recorded by the HD firmware

## Slide 36: EC Backfill
August 2017 – encountered a bug in how backfilling is handled in EC pools
  http://tracker.ceph.com/issues/18162
A read error on an object shard on any existing OSD in backfilling PG will…
  …crash the primary OSD, and the next acting primary, and so on, until the PG goes down
  Misdiagnosis of the issue lead to the loss of an Atlas PG, 23,000 files lost
High disk failure rate coinciding with this bug caused an operational nightmare
  Leaving disks with any pending sectors in is risky
  Bug fixed in Luminous 12.2.3 