## Slide 1: Develop Environmental Sensor Network Case study : Indonesia
Basuki Suhardiman
basuki@Itb.ac.id
Institut Teknologi Bandung

## Slide 2: Outline
Background
Design Model
Protyping and Testing model
Future works and collaboration

## Slide 3: IDeate
By combining the satellite data with meteorological records, Field established that Indonesian fires often occur in association with the ultra-dry conditions in the region that accompany El Niño, a major cyclical weather system. These dry out the underlying peat to the point at which it can catch fire and can’t be extinguished until monsoon rains arrive months later. A next step might be to refine the predictions further by including the combined effects of high temperatures and low humidity on peat moisture, says Field.
He also found that less than 4 millimeters of rain per day during the annual dry season, from August to November – combined with El Niño conditions – seems to be a “tipping point” beyond which fires can to suddenly take off.
https://www.newscientist.com/article/2099496-indonesian-fires-sent-huge-smoke-plume-halfway-around-the-globe/?utm_medium=Social&utm_campaign=Echobox&utm_source=Facebook&utm_term=Autofeed&cmpid=SOC%7cNSNS%7c2016-Echobox#link_time=1470082665

## Slide 4: Fire Report on Mar 2018
http://fires.globalforestwatch.org/report/index.html#aoitype=PROVINCE&dates=fYear-2018!fMonth-3!fDay-8!tYear-2018!tMonth-3!tDay-15&aois=Aceh!Bali!Bangka-Belitung!Banten!Bengkulu!Gorontalo!Jakarta%20Raya!Jambi!Jawa%20Barat!Jawa%20Tengah!Jawa%20Timur!Kalimantan%20Barat!Kalimantan%20Selatan!Kalimantan%20Tengah!Kalimantan%20Timur!Kepulauan%20Riau!Lampung!Maluku!Maluku%20Utara!Nusa%20Tenggara%20Barat!Nusa%20Tenggara%20Timur!Papua!Papua%20Barat!Riau!Sulawesi%20Barat!Sulawesi%20Selatan!Sulawesi%20Tengah!Sulawesi%20Tenggara!Sulawesi%20Utara!Sumatera%20Barat!Sumatera%20Selatan!Sumatera%20Utara!Yogyakarta&dataSource=gfw&reporttype=indonesiaspecialtyreport

## Slide 5: Define
What we (Indonesia) need it ?
  Automated Weather Station
    Rainfall
    Temperature
    Humidity
  Air quality Index and Polution Standard index measurements
    NOx, SOx , CO , NH3 , O3 , CH4 and PM 2.5 (10)
  Sensors and sensors network
  Prediction models (computing capacity)
  Socialize to peoples
https://en.wikipedia.org/wiki/Pollutant_Standards_Index

## Slide 6: Contraints/obstacle
In the field
  There is no power
  Limited converage by telecommunications system
  No sensor available
Source of the fire
  More than 50 km from nearest town

## Slide 7: Build Prototype
Build prototype for AWS+sensor base on Arduino
  Board (I/O)
  Communication
    GSM/GPRS/Wifi
    Ethernet
    USB/Storage System
  Sensors
    Temperature
    Wind speed
    Wind direction
    Humidity
    Rainfall rate
    CO
    Particulate Matters 2.5 and 10 Micron
    CH4 ?
Develop Service Oritented Services (SOA) for the
Put the AWS+Sensors in the area with near forestry/ peatland

## Slide 8: WEATHER DATA RECORD AND COLLECTION TROUGH TCP/IP NETWORK IMPLEMENTATION
A MODEL OF WEATHER MONITORING WITH ARDUINO base SENSORS AND RASPBERY CPU

## Slide 9: Introduction
Background
Internet of Thing consist of set of devices and systems that interconnected sensors and actuators to the Internet. The systems consist of different system. In this presentation we will show the arduino sensors and mqtt software implement on a weather monitoring system and the data should show on Internet.
As the background of choosing this application is the weather data should be more benefit for human life if the data should receive immediately and the weather data collection still limited on a small area or city, hence in a wide area like at plantation or agriculture area in Indonesia,they required collected the data by themself from local weather station manually, because the weather monitoring station prepare by the government still lack at agriculture area, plantation area etc..
There is a demand to collect data from field, then in a year the data should be calculated the rain volume average, climate type and other parameters to fullfill the activity demand. In a wide area with lack of data communication facility will require a data communication facility installation like weather station we tested. The weather data should send trough a gsm cell phone facility from weather station to a server on the base station. Then from base station the data should distributed to Internet.
We hope this weather monitoring equipment model should be use by government or private instritution in the future to fullfill their weather data requirement and they could share it on Internet for their neighbour people or institution.
The weather monitoring station should record weather data per time periode automatically. It built from arduino cpu and mqtt server, gsm modem and raspbery cpu. The data send via gsm network to a web server, then web server distribute it to Internet.

## Slide 10: Prototype 1.0 (2017)
Arduinno
Microcontroller
AWS
-Wind Direction
-Wind speed
-Temperature
Humidity
Rain fall
CO sensor
And other sensors
GSM/GPRS Modul
GPS modul
USB /Storage
ITB
Web Server
For collecting data
And
Portal
Middle Ware
NASA/NOAA web server ,etc
TCP/IP
Forestry (School)
Network of Science Community

## Slide 11: IOT Architecture
Choose of the purpose

## Slide 12: Integrated System by WSO2
Choose of the purpose

## Slide 13: Methodology
The architecture model
Free BSD Server +
Apache + TCP/IP
UTP Cable OR
Wireless LAN
Mobile weather
Sensors include Ethernet and TCP/IP and GSM modem
RASPBERY CPU
SENSOR
ARDUINO
MQ Telemetri Transport
The above is a system with simple web server.
Components : weather sensor (air temperature, wind direction, wind velocity, altitude, and longitude), arduino, gsm module, raspberry pi, FreeBSD server with Apache Web Server
GSM Network
Smart Phone

## Slide 14
The above model is the mature system with WSO2ESB proxy and Web Server. It should receive data from more weather equipment.
Mechanism Data Collection, Send, Record and Distributed to Internet
The sensors will measure the environment parameters, it send to MQTT server, and by raspbery it send to FreeBSD server via TCP/IP network. It should also send to GSM smartphone.
On the FreeBSD server, the txt format file data processed by stream editor and awk program become xml format file. The file then presented by apache web server on the internet. If there will more sensors implemented, the web server should added with wso2esb which act as proxy between mqtt server and web server.
Free BSD Server +
WSO2ESB +Tomcat Web Server + TCP/IP
UTP Cable OR
Wireless LAN
Mobile weather
Sensors include Ethernet and TCP/IP and GSM modem
RASPBERY CPU
SENSOR
ARDUINO
MQ Telemetri Transport
GSM Network
Smart Phone

## Slide 15: Arduinno
Arduinno Mega 2560
  Atmega 2560 ,
  Ram 8 Kbytes
Digital Input
  GPS
  GPRS
  CO /CH4
Analog input
  Humidity
  Temperature
  Pressure
  Rainfall rate

## Slide 16: Testing on the Lab
AWS
  Windspeed, wind direction, temperature, pressure, humidity, CO2 sensor ,etc
  GSM /GPRS

## Slide 17: Hardtest
18 meter above ground
Parameter
  Unitx, date , time (GMT), alt, longitude, height, wind direction , wind speed, rainfall,
  temperature ,humidity , pressure , CO2 , CH4
Push the data to IOTserver
Middleware server (WSO2)

## Slide 18: Stream Data to server
Data :
  Per minutes
  Push the data to the IOT server (MqTT)

## Slide 19: Compare data with earthnull
CO2
400 ppmv
CO2
414 ppmv
https://earth.nullschool.net/#current/chem/surface/level/overlay=co2sc/orthographic=-255.00,0.00,1112/loc=107.698,-6.763
Bandung

## Slide 20: Compare data with earthnull 17-03-2018
Problems with
CO2 Sensor

## Slide 21: Running Operational Test
Start on July 2017 – Nov 2017
  Cause of hardware failure
  AWS sensor on
    Humidity sensors
Started again on Feb 2018
  Problems with
    CO2 sensor , CO and Methane (CH4)

## Slide 22: Data Capture on Oct 2017
date | time | loc | Height (m) | Wind dir (0-360) | Wind speed (m/s) | Rainfall rate (mm/hour) | Temperature (Celc) | Humidity (%) | Pressure (barr) | CO2 | CO
2.10.2017 | 61057 | 10761021 | 807.5 | 225 | 0.4 | 2.5 | 26.7 | 99 | 921.0 |  | 389
 | 61158 |  |  | 225 | 0.9 | 2.5 | 26.1 | 99 | 921.2 | 391 | 333
 | 61259 |  |  | 270 | 0.9 | 2.5 | 25.6 | 99 | 921.1 | 392 | 456
 | 61400 |  |  | 270 | 1.3 | 2.5 | 25.6 | 99 |  | 391 | 385
 | 61501 |  |  | 225 | 0.9 | 2.5 | 25.6 | 99 |  | 393 | 674
4.10. 2017 | 34436 |  |  | 0 | 0.4 | 0.0 | 29.4 | 79 | 923.4 | 393 | 300
 | 34537 |  |  | 90 | 0.4 | 0.0 | 28.9 | 80 | 923.5 | 393 | 400
 | 34638 |  |  | 270 | 0.0 | 0.0 | 28.9 | 80 |  | 389 | 329

## Slide 23: Problem Occur
Sensors
  Availabilty in contiunues operation in long term
    Humidity sensor has broken
Calibration methods
  Compare with other standard measurements
Standard Calibration
  Methane (CH4)
  CO
  CO2

## Slide 24: Model vs real world
Symbolic model
Real World
Data
Model 1
New Data
Evaluation : No Good
Model 2
New Data
Model 3
New Data
Evaluation : Poor
Evaluation : OK
The decision making process. Design for Decision by Irwin Bros, 1953 by Macmillian

## Slide 25: Collaborate
ASGC (TW) for running the simulation model for firewatch (DMCC program)
  WRF-Fire
  WRF-Chem
  Virtualization, remote access
Ministry of Forestry and Environment
  Put AWS+Sensor in peatland areas
Open the data on Public Server

## Slide 26: Future Works (collaboration)
Data sharing
  Data are available only in web based information systems
  Need to develop web services to make those data available to others
    http://weather.meteo.itb.ac.id/aws.php is one example that have some of their data available to others using web service (by request)
Build the model for reduce impact on Disaster
  Fire on Forestry / Land fires
  CO/CO2 models
  PM (Particulate Mattes 2.5 micron)
Build the Sensor Network
  AWS (Automatic Weather Station)
  Carbon Monoxide (CO)
  Carbon Dioxide (CO2)
  Particulate Matter
  Methane
Need Collaboration for
  Callibration for the sensors network
  Calibration for the Sensors

## Slide 27: Thank You

## Slide 28: References
http://fires.globalforestwatch.org/home/
http://weather.meteo.itb.ac.id/awsmap.html
https://www.slideshare.net/wso2.org/io-t-referencearchitecturewebinar
https://www.slideshare.net/Nibodha/enterprise-architecture-and-iot
http://www.iotarchitecturegroup.com/
https://wso2.com/whitepapers/a-reference-architecture-for-the-internet-of-things/
http://standards.ieee.org/develop/wg/IoT_Architecture.html
https://www.ibm.com/developerworks/library/ws-mqtt/index.html
https://lynx2015.files.wordpress.com/2015/08/arduino-mega-pinout-diagram.png