## Slide 1: Using Virtual Internet Exchange Point to Build Layer 3 Network Testbed: A Study Case
Reporter: Wen-Ju Chiang

## Slide 2: OUTLINE
Motivation
Testbed Architecture
Use Case
Future work

## Slide 3: OUTLINE
Motivation
Testbed Architecture
Use Case
Future work

## Slide 4: Motivation
In recent years, the information, cyber-security and network function virtualization have become increasingly important in network operation and management.
While these changes have brought impacts on network research and education, especially for internet innovations.
Playing only with multiple VM and forwarding localhost packets shall not be the only option for a student.

## Slide 5: Motivation (cont.)
Students are struggled
  Lack of compute resource
    A server, switch or router is way too expensive for an individual
    Second hand might be a choice, how about power or storage cost?
  Lack of real world packets
    You can control what you send or receive within your local network
    There will always be someone bombs you with unexpected packets
  Method to connect with others
    While coding is important in programming
    Communication, negotiation and cooperation is more important in networking

## Slide 6: Motivation (cont.)
As a student, if you want to advertise your own IP prefix and connect to the world, you are required to.
  Have your own AS Number ($70/year)
  Have a running server 24/7 ($60/year)
  Have an IP Prefix ($720/year for IPv4, $5/year for IPv6)
  Monitor your network
These are costly and time consuming for a normal student.
How to provide a platform for student with hands on experience to connect and tackle with real world alike environments and problems.

## Slide 7: OUTLINE
Motivation
Testbed Architecture
Use Case

## Slide 8: IXP Manager
IXP Manager is an open-source management platform designed for Internet Exchange Points (IXPs). It provides tools for managing peering networks, automating configurations, monitoring traffic, and improving operational efficiency at IXPs.
Benefits
  Automated Configuration
    Generates BGP, route server, and switch configurations.
  Traffic Monitoring & Reporting
    Provide user-friendly UI/UX for real-time analytics.
  Security & Access Control
    Supports authentication, role-based access, and security best practices.

## Slide 9: Virtualized Internet Exchange Point
Create a Virtualized Internet Exchange Point (VIXP) with a real world uplink.
Every users can advertise their own IPv6 address in order to gain internet access.
VIXP (AS65000)
AS214821
user
user
user
user
Aggregate prefixes
Replace private ASN to public ASN
Internal Traffic
Internal Traffic
Only /64 are provided to students due to lack of IPv6 suffixes
Firewall
Making sure that users doesn’t misconfigure and impact public network

## Slide 10: Architecture
VIXP (AS65000)
IXP Manager
Dynamic
Configuration
Return Status
Route Reflector Router
Linux bridge
User Connect Point Containers
User Connect Point Containers
User Connect Point Containers
User Connect Point Containers
Uplink Router (AS214821)
Internet
Users are able to connect to the VIXP via user connect point containers
Manager
Dynamically Spawn
Configure
VPN
Create VPN if needed

## Slide 11: OUTLINE
Motivation
Testbed Architecture
Use Case
Future work

## Slide 12: ONOS
Open Network Operating System (ONOS) is an open-source SDN (Software-Defined Networking) controller designed for high availability, scalability and performance.
Benefits
  Programmability
    Allows dynamic network management via APIs and applications.
  Scalability
    Supports distributed architecture for handling large-scale networks.
  Features
    Intent for easy programming
  Open-Source

## Slide 13: OVS
Open vSwitch (OVS) is an open-source, high-performance virtual switch designed to enable network automation, support SDN protocols (like OpenFlow), and optimize traffic in virtualized environments.
Benefits
  SDN Support
    Works with SDN controllers
  Features
    Provides GRE, VXLAN, QoS etc.
  Open-souce

## Slide 14: Networks with Physical Routers
Physical routers
  1. Deal with routing decision.
  2. Deal with gateway exchange.
Every edge requires a router, running eBGP and iBGP protocols.
AS 65000
AS 65001
AS 65002
Switch
Switch
AS 65003

## Slide 15: SDN Networks with Virtual Routers
SDN-enabled Virtual Routers
  Doesn’t requires router connection to edge.
  Only one BGP speaker is enough.
  Doesn’t need a real gateway.
AS 65000
AS 65001
AS 65002
OVS1
OVS2
AS 65003
BGP Speaker
(FRRouting)

## Slide 16: Virtual Router BGP Connection
Physical router:
  External routers connect with the boarder gateway.
Virtual router:
  External routers connect with BGP Speaker.
  Need to delegate BGP Speaker IP to edge switch.

## Slide 17: SDNFV Training Platform
Software-Defined Networking & Network Functions Virtualization (SDNFV) is the combination of SDN (Software-Defined Networking) and NFV (Network Functions Virtualization) to create a more flexible, automated network infrastructure.

## Slide 18: SDNFV Training Platform
Software-Defined Networking & Network Functions Virtualization (SDNFV) is the combination of SDN (Software-Defined Networking) and NFV (Network Functions Virtualization) to create a more flexible, automated network infrastructure.
SDN (Software-Defined Networking)
  Separates the control plane (decision-making) from the data plane (packet forwarding).
  Uses SDN controllers for centralized network management.
  Enables programmability and automation of network traffic flow.

## Slide 19: SDNFV Training Platform (cont.)
Software-Defined Networking & Network Functions Virtualization (SDNFV) is the combination of SDN (Software-Defined Networking) and NFV (Network Functions Virtualization) to create a more flexible, automated network infrastructure.
NFV (Network Functions Virtualization)
  Moves traditional network functions (e.g., firewalls, routers, load balancers) from hardware appliances to virtualized software running on standard servers.
  Uses Virtual Network Functions (VNFs) to replace dedicated network devices.
  Reduces dependency on expensive proprietary hardware.

## Slide 20: SDNFV Training Platform (cont.)
SDNFV is taught in National Yang Ming Chiao Tung University (NYCU) by professor Chien-Chao, Tseng.
This class aims to
  Enhance students with knowledges of SDNFV
  Using OVS and ONOS to provide SDN network environment
  Provide students with hands on experience with network management via NFV
Final Project of the class
  Provide a virtual Router (vRouter) to emulate router function.
  Create a Layer 3 network environment that can route the packet to the intended destination and drop unauthorized packets.

## Slide 21: Project Architecture
Students are grouped to also peer with each other
VIXP (AS65000)
stu-group 01
stu1
stu2
stu3
stu-group 02
stu4
stu5
stu6
A
B
C
Students will form a group of 3.
Members in each group shall peer with each other.
Every student will connect to the VIXP.

## Slide 22: Project Target
Students are required to produce a vRouter with SDN.
Students are required to deal with
  Intra-domain Traffics
    Hosts within the same AS communicates with each other
  Inter-domain Traffics
    External host communicates hosts within student’s AS
  Transit Traffics
    Traffics bypass student’s AS during communications between hosts
In this project, students are their own ISP, which is required to peer with others, transit others traffic and provide QoS capability.

## Slide 23: Project Target (cont.)
Training students with layer 3 network knowledges and experiences
  Providing an environment for student to configure their own network settings
  Transform knowledge in books to hands on ability
  Students shall provide self protection in their application to not been effect by others within the network
Introducing real-world internet resources for students
  Students are able to connect their SDN project to IXP for practicing and exploring BGP, SDN, NFV with allocated IP resources
  Learn the value of public IP resources

## Slide 24: Project Topology as a Group
AS65xx0 (SDN Network)
ONOS
VXLAN
FRRouting
Host 1
VXLAN
AS65000
AS65xx1
Host 2
AS65yy1
Host 2
AS65yy0 (SDN Network)
ONOS
VXLAN
Host 1
FRRouting
TA
1Gbps Rate Limit
Student x
1Gbps Rate Limit
Student y

## Slide 25: Project Topology as a Student
AS65xx0
ONOS
VXLAN
AS65xx1
Host 2
172.17.xx.1/24
2a0b:4e07:c4:1xx::1/64
172.17.xx.2/24
2a0b:4e07:c4:1xx::2/64
OVS1
OVS2
OVS3
192.168.100.2/24
VXLAN
FRRouting
192.168.63.2/24
fd63::2/64
192.168.60.xx/24
192.168.61.xx/24
AS65000
172.16.xx.2/24
2a0b:4e07:c4:xx::2/64
Host 1
192.168.70.253/24
fd80::fe/64
192.168.63.1/24
192.168.70.xx/24
172.16.xx.69/24
192.168.100.3/24
fd63::1/64
fd70::xx/64
2a0b:4e07:c4:xx::69/64
1Gbps Rate Limit
TA
Also FRRouting

## Slide 26: Project Configurations
Students are running an AS65xx0 and announcing prefixes
  172.16.x.0/24.
  2a0b:4e07:c4:xx::/64
Students help to transit prefixes announced by AS65xx1
  172.17.x.0/24.
  2a0b:4e07:c4:1xx::/64
IXP is AS65000 at 192.168.70.253/24 and fd70::fe/64
  Students have to announce the prefixes you know to the IXP
  Students can connect the IXP via
    192.168.70.x/24
    fd70::x/64

## Slide 27: Testing Requirements
For service customers (AS65xx0 SDN Network, host 1)
  Able to ping FRRouting’s IP (172.16.xx.69/24). (Intra-domain Traffic)
  Able to ping student y’s FRRouting’s IP (172.16.yy.69/24). (Inter-domain Traffic + Peering)
  Use https://tools.keycdn.com/ipv6-ping to see ICMP replies. (Inter-domain Traffic + IXP Connection)

## Slide 28: Testing Requirements (cont.)
For transit ISP (AS65xx1, host 2)
  Able to ping host 1 IP (172.16.xx.2/24). (Inter-domain Traffic + Peering)
  Able to ping student y’s FRRouting’s IP (172.16.yy.69/24). (Transit Traffic + Peering)
  Able to ping student y’s host 2’s IP (172.17.yy.2/24). (Transit Traffic + Transit)
  Use https://tools.keycdn.com/ipv6-ping to see ICMP replies. (Transit Traffic + IXP Connection)

## Slide 29: IXP Manager Looking Glass
You can see what you have announced via IXP Manager
Your ASN
Your x
Click to see what you have announced

## Slide 30: Expected Result
Students can test that they have connected to the outside world

## Slide 31: Further Experiment
BGP hijacking
  A takeover of IP prefixes by manipulating the Border Gateway Protocol (BGP) by advertising prefixes that does not belongs to it.
The attack is performed to the students within the network
  Student’s packet are forwarded to malicious servers.
  Student are required to provide method to prevent hijacking
Attack influence scope
  The attack is only taking affect within the testbed.
  Blocked by the firewall and doesn’t leak to the real world.

## Slide 32: OUTLINE
Motivation
Testbed Architecture
Use Case
Future work

## Slide 33: Testbed Internal Protection
A switch loop is created within a group, since students have created the router and there are no switch loop protection.
Which results in
  Broadcast storm is formed within the testbed.
  All students received tremendous broadcast packets, leading to their own computer failure.
Network resource collisions
  MAC Address
  IP
These doesn’t effect the core system, but is a problem to other users; therefore, an internal protection/alert system shall be introduced.

## Slide 34: Q&A
Thank you for your attention