## Slide 1: Performant Perimeter Security: A Foundation for Data Intensive Science
ISGC 2026
Taipei, Taiwan
19 March 2026
Eli Dart
Network Engineer, Science Engagement
dart@es.net

## Slide 2: Our World Is Data-Centric
Many, many scientific discoveries are impossible without data analysis
Modern science relies on computing, data, storage, all interconnected using fast networks
ESnet even thinks of itself as a “data circulatory system”

## Slide 3: Most People Want Semantic Reasoning
Think about high level analysis instead of low level data sets
This is where the value is
This is where the discoveries are
However, in order for this to be possible, the low level stuff has to work
Image: Olawumi, Mattew & Oladapo, Bankole & Olugbade, Temitope & Omigbodun, Francis & Olawade, David. (2024). AI-Driven Data Analysis of Quantifying Environmental Impact and Efficiency of Shape Memory Polymers. Biomimetics. 9. 490. 10.3390/biomimetics9080490.

## Slide 4: Data Infrastructure Under The Semantics
ESnet supports the DOE scientific research ecosystem.
Interconnects all US national labs and user facilities
Provides reliable, high-performance connectivity to global research collaborations, the Cloud, and the larger Internet.
Notes: In short: ESnet is a high-performance, high-speed network that serves as the “data circulatory system” for the DOE scientific research ecosystem, connecting the 17 national labs and 28 other user facilities (soon to include the High Performance Data Facility), plus CERN in Switzerland.
This map just shows ESnet’s US and European backbone. It also peers with more than 270 research and commercial networks, transmitting data traffic all over the globe.
ESnet's vision is that scientific progress will be completely unconstrained by geography — the physical location of instruments, people, computational resources, or data should not matter.

## Slide 5: Science Needs More Than Just The Network
Computing and storage
  HPC center, institute
  cloud, personal device
Code (workflow, analysis, …)
All of these things exist somewhere in physical space
All of these things located in the network topology
It’s great to be able to reason at a higher level
  But then all the lower level stuff has to work!
Science workflows are multi-domain in the general case
Data and workflows cross network boundaries

## Slide 6: What is Perimeter Security?
Network perimeter: boundary between zones of control
Each organization has its zone of control
  Hardware owned by the organization
  Network topology under the control of the organization
  Connection of the network to the outside world
Cloud complicates this, but the network perimeter still exists
  This is a necessary construct
  ZeroTrust doesn’t change it
  On-premise assets are “inside” the perimeter, the rest of the Internet is “outside” the perimeter
We can think of perimeter security as the policies and technologies that defend on-premise assets from network-based attacks

## Slide 7: Science Crosses the Perimeter
Science collaborations are inherently multi-domain
  Labs, Universities, Cloud, etc.
  Data must move between sites and resources
Science mission requires that high performance science traffic moves between and across zones of control
  Data, computing, storage, instruments, researchers
  All are at different locations in the network topology
Key point: high performance data flows have a concrete location in the network topology
  Virtualization, cloud, workflows, etc. all hide physical performance characteristics, but that doesn’t change them
  If we want workflows to perform, we have to have a performant physical path for the data

## Slide 8: Security and Performance In Conflict
The organization must defend its perimeter
  Huge liability risk
  Operational/availability risk
  This MUST happen, so it WILL happen!
  We can choose how it happens, but not whether it happens
Science requires performance
  In order to meet the science mission, we must find a way to make data flows performant
  Because perimeter security must exist, performance must exist in the context of perimeter security
  Find a way to run high performance workflows across the perimeter

## Slide 9: High Performance, Safely
This is both a technical issue and a sociological issue
The technical solutions must be technically sound
However, policy is critical, and there are multiple related but separate aspects to perimeter policy
  Which hosts/systems are allowed to exchange data?
  Which applications and protocols are permitted?
  Which technologies are used to enforce policy?
The answers to these questions determine whether high performance data applications can use your perimeter
  And: can your scientists run high performance workflows at your site, using your computing, instruments, and storage?

## Slide 10: Best Practice: Science DMZ
The answer is the science dmz model.
  Separate high performance science traffic from enterprise traffic
  Build the science data perimeter using performant technologies
If we can do this, we can scale up data performance to match the data scale

## Slide 11: Limitation Is An Enabler
Only approved services in the Science DMZ
  Services that can be secured with stateless firewalls
  Complexity is the enemy
Allows space for performant security
Control vs. Data can be handled separately
  Enterprise firewall is fine for control messages, auth, etc.
  Need Science DMZ for high performance data

## Slide 12: Lessons Learned Over Time
Enterprise security team will try to eliminate Science DMZ
  “The firewall is faster now”
  “The DMZ isn’t secure because it doesn’t have a firewall, so we will put in a firewall to make it secure”
  Multiple variations of this
Workflows change over time
  You may not know about the changes in advance
  Science need drives mission
  Architecture must accommodate changes needed by science
Must find a way to make performance persistent
  Then, users can rely on it

## Slide 13: Lessons Learned Over Time (2)
Most users won’t ask for help
  They just suffer in silence or change to fit limitations
  Many “know” that things can’t be better
Proving a negative is hard
  Very difficult to find evidence that users would be doing better if they could
Answer: build it right, and teach users to use it
The results can be impressive

## Slide 14: A Note About Data Locality
I hear a lot of people say “don’t move the data”
  “Just move the compute to the data!”
Of course! Do that if you can. But there are often difficulties
  Open access data, closed access computing
    Code execution is often tightly controlled
    Scientist often doesn’t have permission to run analysis next to the existing data store → need to move the data
  Specific hardware required
    Specialized systems, computing scale, other requirements
    Move the data to the specific system
  I don’t have to pay to run on my local system
    More creativity if I run there
    I have to move the data to my cluster
Therefore, we must support data movement in the general case

## Slide 15: What is Possible?
I’m going to go through a few real-world examples
  High performance data workflows across the perimeter
  Multiple Science DMZ design pattern examples
First examples: file transfer using DTNs
  Classical use of Science DMZ
  Transfer files or objects from one storage system to another
  Valuable if data needed at remote location for some time
  Many, many workflows do this
Basic portal or cluster/HPC implementation of Science DMZ

## Slide 16: Portal Design Pattern

## Slide 17
Shown: Status as of March 10, 2022
4 to 6 GB/s
1.5 GB/s
Replication: Globus used to move 7.4 petabytes of data from Livermore to Argonne and Oak Ridge Labs
To ALCF
To OLCF
17,347,671 directories and 28,907,532 files
From February 12 to May 4, 2022
Slide credit: Ian Foster, ANL

## Slide 18: Replication: Transfer Strategy
Keep the slow part busy
  Sync between the fast systems
  Fail over during maintenance windows
Note performance differences
  Outbound from LLNL much slower
  Sync between ALCF and OLCF is fast

## Slide 19: Portal Data Replication: Discussion
Data portal infrastructure already had DTNs in place
All the replication team had to do was use them
If they had had to use the portal web server, the task would have been impossible
New use for the DTNs, very valuable to have them there

## Slide 20: HPC/Cluster Design Pattern

## Slide 22: Large Scale Data Transfer
Two Globus transfers from OLCF to NERSC were started by the same user (presumably for the same project – DESI – which is dark energy/cosmology) within 40 minutes of each other.
  One transfer was ~350k files, ~296TB
  Other transfer was ~1.8M files, ~472TB
  Data transfer rate peaks over 80Gbps
  Total transfer volume ~768TB
  Total wall clock time ~39 hours
Current tools (Filesystems, DTNs, Globus) handle petascale data sets easily

## Slide 23
Small job (296TB)
Big job (472TB)
Total volume in two jobs: 768TB
OLCF Globus endpoint pause (scheduled maintenance)

## Slide 24: Key Points
Sophisticated tools bring multiple benefits
  Both transfers experienced random data corruption (multiple checksum failures) which was automatically corrected by Globus (data set is ¾ of a petabyte….a lot can happen with that much data)
    User had to expend zero effort to find and fix the corrupted files
  OLCF endpoint paused for a workday for normal scheduled maintenance, and transfer resumed after maintenance concluded
    OLCF staff did not have to worry about the user when planning maintenance
    User had to expend zero effort to work around HPC facility maintenance
  Easy to use tools with automated fault recovery reduce human effort
Large scale data transfer is a key enabler for scientific productivity
  Benefits of large-scale HPC allocation brought back to collaborators
Normal, routine operations – no magic

## Slide 25: Large Scale Replication From Cloud
Notes: Cloud to science institution

## Slide 26: Large Scale Replication From Cloud
Rubin/LSST project at SLAC
Large scale data replication
  250M files
  Over 2.3PB
  Approx. 8.5 days
Six DTNs at SLAC
  K8 environment
  Google Cloud Storage Transfer application
Traffic traversed three Squid proxies at SLAC

## Slide 27: Google to SLAC Replication - Key Points
Petascale data transfer from cloud works!
Small number of DTNs can achieve good performance
Containers are viable for high performance applications, including I/O intensive

## Slide 28: File Transfer: Discussion
When the infrastructure is already in place, users just use it
  Nobody has to ask permission
  No complex config for users to do
  No need to debug the end to end path before using it
Users can concentrate on the workflow
Simple protocols, high performance
  Simple policy: Support DTN driven data transfers
  Simple protocols: Globus, cloud-native object access, etc.
  Safe to operate when secured with performant technologies, in keeping with Science DMZ

## Slide 29: Storage Becoming A Limitation
Image: Raj Kettimuthu, ANL
In many cases, storage I/O is now the bottleneck
Answer: streaming
One or both ends of the data transfer is volatile
  Instrument
  Memory
Removes storage limitations from the workflow

## Slide 30: Stream From Site Storage To Cloud
Workflow reads from site storage into cloud analysis job
No local storage in the cloud environment
  Compute job analyzes the data and then drops it
  Need the data again? Fetch it again!
  No cloud storage costs
High performance perimeter required for success
  Packet loss or other network issues reduce compute performance
  Easy to do with Science DMZ
Two examples follow

## Slide 31: Analysis in Cloud: Vera Rubin Observatory
Two parts to Rubin workflow
Acquisition + alerting
  Data comes from the telescope in Chile to SLAC in USA
    World’s largest digital camera on telescope in Chile
    Data path traverses many networks, including ESnet
    Prompt analysis and alert generation at SLAC
  Multinational networking collaboration required to get the data to SLAC
  Alerts sent to scientific community
User analysis
  Data releases distributed from SLAC to scientists
  Jupyter analysis environment for users in Google Cloud
    Cloud job reads data from SLAC into Jupyter notebook
    Collaboration will scale this up as data accumulates

## Slide 32: Rubin Data Management System includes both making data and serving data to users
Notes: Rubin services are deployed via kubernetes - “configuration as code”
Makes it easier to deploy in different places
  RSP is running in at least 6 locations: IDF, NCSA, Summit, FrDF, UKDF and SLAC
  RSP users live in a Rubin-controlled containerized bubble
Catalogue access is via a TAP service (no direct querying of Qserv)
  Traffic load is not seen as large; access SLAC’s Qserv from cloud RSP (and Chile’s)
Most Rubin data will be in object stores
  Access is via url - will be signed and timed to limit to data rights holders
  Can access SLAC’s archive from the Cloud if users need more than Coadds
  100 Gb/s link between SLAC and Google today

## Slide 33: Training and Inference in Commercial Cloud
DUNE collaboration
ML based data reduction
Near-real-time inferencing classifiers supporting neutrino physics workflows.
Hybrid workflow
  Data and CPU computing at FNAL
  GPUs in Google
Impossible without high performance perimeter
Works great if you do have high performance perimeter

## Slide 34: Data From Lab to Cloud For Inference
~80Gbps for hours at a time
Over 1PB moved in ~30 hours
No need to replicate the data first (no file transfer workflow)
No in-cloud storage costs

## Slide 35: Site to Cloud Streaming: Discussion
Data storage and servers are on infrastructure owned by the community/collaboration
  Storage systems with DTNs
  POSIX or object store, doesn’t matter
Analysis/compute clients in the cloud fetch the data directly
  No copying to cloud storage first
  Just read the data in from remote storage, analyze it
Site perimeter design: DTNs for outbound data
  Simple security policy (address and port filters)
  Safe to operate with performant security technologies
Science workflow requires high performance
  Scaling enterprise firewalls to support this is difficult and expensive
  No added benefit from enterprise firewalls (just address/port)

## Slide 36: Stream From Cloud To HPC
These workflows go in the other direction
Data comes from the cloud, across the perimeter, and into a running analysis job on a supercomputer
Can be many many nodes on both sides
Bandwidth can get quite large
Not limited by HPC storage I/O
  No need to wait for data replication
  Workflow can go faster than the DTN cluster

## Slide 38: Direct Transfer to Compute: Amazon to NERSC
Data set in commercial cloud
Weather forecasting code
No replication before job launch
Direct ingest by compute job takes pressure off the HPC facility storage system

## Slide 39: Many cloud servers to a few compute nodes

## Slide 40: Direct Transfer to Compute: Google to NERSC
Large (over 5PB) public data set in commercial cloud
  ECMWF ERA5
  AI-ready
ML-accelerated earth system model application
Direct data ingest into running code

## Slide 41: Flow statistics: massively parallel
Host breakdown:
  Many, many parallel streams in these transfers
Many cloud hosts delivering over 10Gbps
User was able to just launch the job and move forward.
  No special setup
  No debug before use

## Slide 42: IPv6 Works!
A lot of this transfer occurred over IPv6
It was already set up and configured - no need for user to care
IPv6 is real now, even in commercial cloud environments

## Slide 43: Evolution Of Data-Intensive Science
Science DMZ enabled high performance file transfer
  DTNs
  Performant tools
Now, we are running into the limitations of storage
  File transfer before job launch increases friction
  Storage layer is slow and expensive
New workflows drive ever higher performance across network boundaries
But this only works if the perimeter is performant

## Slide 44: In conclusion – ESnet’s vision:
    Scientific progress will be completely unconstrained by the physical location of instruments, people, computational resources, or data.

## Slide 45: Thanks!
https://my.es.net/
https://www.es.net/
https://fasterdata.es.net/
Eli Dart
dart@es.net

## Slide 46: Thanks!
https://my.es.net/
https://www.es.net/
https://fasterdata.es.net/
Eli Dart
dart@es.net