## Slide 1
TreeLine
Compiling Random Forest Classifiers
to SmartNIC Hardware Pipelines
Wen-Ju, Chiang
WinLab, Dept. of Computer Science, NYCU
ISGC 2026 — Networking, Security & Operations
March 20, 2026 · Academia Sinica, Taipei
BlueField-2 DPU
DDoS Detection
Line-Rate

## Slide 2
The Challenge
Volume
3.5 Tbps
Record DDoS (2024)
Latency
> 100 µs
CPU ML inference
Cost
CPU $$
Wasted compute
Can we run ML classifiers on the SmartNIC — at line-rate?

## Slide 3
DDoS Detection: Evolution
From signatures to hardware-accelerated ML
Gen 1
Signature / Rate-Limit
+ Simple, low cost
- Zero-day blind, high FPR
Gen 2
ML on CPU / GPU
+ Adapts new attacks
- > 100 µs latency, CPU bottleneck
Gen 3
ML on Other Devices
+ Line-rate, zero CPU
- Limited model complexity
This work

## Slide 4
Existing Solutions: All Roads Lead to P4 Switches
System | Venue | Platform | Limitation
pForest | ETH 2019 | Tofino P4 switch | $15-30K dedicated HW
NetBeacon | USENIX Sec '23 | Tofino P4 switch | Same
Planter | SIGCOMM CCR '24 | Tofino P4 switch | Same
BoS | NSDI '24 | Tofino P4 switch | Same
SmartTC | IWQoS '25 | BF-3 ARM cores | Software, ~5 Gbps
TreeLine (this work) | — | BF-2 HW pipeline | First on DOCA Flow
Every prior in-network ML system requires Intel Tofino P4 switches ($15-30K each)
NVIDIA BlueField DPUs are already deployed at scale (Azure, GCP) — but no one has used the hardware pipeline for ML

## Slide 5
Why Random Forest?
Properties that enable hardware compilation
RF Advantages
vs. Deep Learning
Binary splits → if/else in HW
Independent trees → parallel pipes
Majority vote → simple aggregator
No matrix ops → no GPU needed
Interpretable → debuggable rules
Matrix multiply → needs GPU/NPU
High latency (> 100 µs on CPU)
Black box → hard to audit
Overkill for flow classification
Cannot run on eSwitch HW

## Slide 6
The Throughput Gap
High Accuracy / Low Throughput
Trade-off Zone
High Throughput / Low Accuracy
Deep Learning
GPU/CPU needed ~1 Gbps
Random Forest
CPU-bound
~5-10 Gbps
Rule-based / ACL
HW line rate
~100 Gbps
TreeLine
ML accuracy at hardware line rate — on existing DPU infrastructure
98.7 Gbps | 99.98% accuracy | 0 CPU cores
Can we get ML accuracy at hardware line rate — without dedicated P4 switches?

## Slide 7
TreeLine Architecture Overview
BF-2 eSwitch (Hardware)
Packet
Tree 0
vote
Tree 1
vote
Tree 2
vote
Tree 3
vote
Tree 4
vote
Aggregator (majority vote)
ATTACK
BENIGN
Compiler
sklearn RF
(.pkl)
rf_to_doca.py
(automated)
DOCA Flow C
build on ARM
5 trees, 75 pipes | 10 per-packet features | Fully automated | < 1s compile, ~3s build
ARM CPU is not in the data path — all classification runs in eSwitch hardware

## Slide 8
DOCA Flow Pipes Are Decision Tree Nodes
Decision Tree Node
if (feature <= threshold):
-> left child
else:
-> right child
DOCA Flow Pipe
if (packet matches entry):
-> fwd (next pipe)
else:
-> fwd_miss (other pipe)
Each tree node maps to one hardware pipe. The mapping is direct — not an approximation.
Multiple trees run independently in chained pipes. Results aggregated by majority vote in a final pipe.

## Slide 9
DOCA Flow API: How It Works
The building blocks TreeLine compiles to
Pipe Types
Basic Pipe: match → action
Control Pipe: ordered rules
Ordered List: priority chain
Match Semantics
Exact: value == field
Ternary: (value & mask) == field
No range → need decomposition
Actions
fwd → next pipe (match)
fwd_miss → next pipe (no match)
set_meta → write u32 register
Metadata Registers
5 × u32 registers (meta.u32[0–4])
Survive across all pipe stages
Used for tree voting results

## Slide 10
Key Insight
Decision tree nodes map 1:1
to DOCA Flow pipe stages
Internal node
Basic Pipe — match + fwd / fwd_miss
Threshold (≥ N)
Ternary mask entries — value & mask in Control Pipe
Leaf node
Counter Pipe — increment class counter

## Slide 11
Model Complexity Has Zero Impact on Throughput
0%
throughput
penalty
Pipe Depth | Throughput (Gbps) | vs Baseline
1 (baseline) | 98.72 | —
5 | 98.72 | 0%
10 | 98.72 | 0%
20 | 98.72 | 0%
40 | 98.72 | 0%
1 pipe or 40 pipes — same throughput at 100 Gbps
1518B packets, T-Rex v3.08, 25-second runs, 202M+ packets, BF-2 eSwitch hardware counters

## Slide 12
Line Rate Achieved at >= 256B Packets
100 Gbps wire rate
47.1
64B*
69.4
128B
76
256B
96.3
512B
98.1
1024B
98.7
1518B
Gbps
*64B limited by generator OVS bridge. DUT processes 86.5 Mpps at wire speed.

## Slide 13
Baseline Comparison
Fair: all optimized C (-O2), same RF model
Platform | Mode | Throughput | Cores Used
TreeLine (BF-2 eSwitch) | HW pipeline | 86.5 Mpps | 0
Host CPU (C+DPDK) | Per-packet, live | 24.3 Mpps | 1
Host CPU (C, batch) | Batch 10M | 42.8 Mpps | 1
BF-2 ARM (C, batch) | Batch 1M | 17.9 Mpps | 1
~4 CPU cores to match TreeLine — or 0 cores with hardware offload

## Slide 14
99.98% DDoS Detection with 10 Per-Packet Features
99.98%
overall accuracy
6 DDoS attack types
15M flows (CIC-DDoS2019)
All types >= 99.95%
10 Per-Packet Header Features
Dst Port, Src Port, Protocol, IP Total Length
TCP Flags: SYN, ACK, RST, PSH, URG, FIN
All directly extracted from packet headers — no flow-level statistics needed
No mean, std, inter-arrival time, flow duration
— those require stateful tracking that hardware can't do
No flow-level statistics needed. Per-packet features alone are sufficient.

## Slide 15
Even 1 Tree at Depth 3 Achieves 99.97%
Config | Accuracy | Pipes | Throughput
1 tree, depth 3 | 99.97% | 12 | 98.7 Gbps
1 tree, depth 10 | 99.99% | 16 | 98.7 Gbps
3 trees, depth 5 | 99.99% | 42 | 98.7 Gbps
5 trees, depth 5 | 99.99% | 74 | 98.7 Gbps
5 trees, depth 15 | 99.99% | 78 | 98.7 Gbps
Throughput is constant — scale model freely

## Slide 16
DOCA Flow on BF-2: What Works (and What Doesn't)
Works
+ Pipe chain >= 64 stages, zero loss
+ >= 10K entries per pipe
+ ~936K entries/sec batch insertion
+ 5 independent metadata registers
+ >= 5 match fields per pipe
+ Ternary threshold matching
Doesn't work
- ACL pipe in switch mode
- TCP window field (not exposed)
- Floating point / arithmetic
- Flow-level stats (mean, std)
- Neural networks, SVM
7 systematic experiments on BF-2, DOCA SDK 3.2 — first characterization of DOCA Flow for ML inference

## Slide 17
TreeLine vs Prior Work
System | Platform | Model | Throughput | CPU Cost | HW Cost
TreeLine | BF-2 DPU | RF | 98.7 Gbps | 0 cores | ~$1-2K (existing)
Planter | Tofino P4 | RF/XGB | ~100 Gbps | N/A | ~$15-30K
NetBeacon | Tofino P4 | XGBoost | ~100 Gbps | N/A | ~$15-30K
SmartTC | BF-3 ARM | ML | ~5 Gbps | 8 ARM cores | ~$2K
CPU+DPDK | x86 host | RF (C) | 24 Mpps/core | ~4 cores | —
P4-switch performance at DPU price, with zero CPU cost

## Slide 18
DPUs Are Already Everywhere
P4 Switch Approach
- Dedicated Tofino switch ($15-30K)
- Per-rack deployment
- Separate management plane
- Not in every data center
TreeLine (DPU Approach)
+ Existing BlueField DPU ($1-2K, already installed)
+ Per-server deployment
+ Standard DOCA SDK management
+ Already in Azure, GCP, every rack
No new hardware — ML inference on infrastructure already deployed at scale
- Perhaps been give up by Intel

## Slide 19
Limitations & Future Work
Limitations
Future Work
Max 5 trees (register limit)
Flow-level feature proxy gap
Single dataset (CIC-DDoS2019)
Throughput & latency bench
ARM-side flow counters
BF-3 (more registers and DPA)

## Slide 20
Key Takeaways
1
Decision trees → pipe chains via fwd/fwd_miss
2
Ternary decomposition for exact thresholds
3
Metadata registers for ensemble voting
4
TreeLine compiler: sklearn → C, automated
5
98.7 Gbps, zero throughput penalty from model complexity
Thank you! Questions?

## Slide 21
Acknowledgment
This work was supported in part by the Center for Intelligent Team Robotics and Human-Robot Collaboration under the “Top Research Centers in Taiwan Key Fields Program” of the Ministry of Education (MOE), Taiwan, and in part by the National Science and Technology Council, Taiwan, under grants NSTC 114-2218-E-011-003 and 114-2221-E-A49-009.

## Slide 22
Backup A: Per-Attack-Type Accuracy
HW-only 10 features, CIC-DDoS2019, 15.1M rows
Attack Type | Samples | Accuracy | F1
DrDoS_DNS | 194K | 100.00% | 100.00%
DrDoS_LDAP | 85K | 100.00% | 100.00%
DrDoS_NTP | 47K | 99.95% | 99.98%
DrDoS_SNMP | 204K | 100.00% | 100.00%
Syn flood | 55K | 100.00% | 100.00%
UDP-lag | 13K | 100.00% | 100.00%

## Slide 23
Backup B: BENIGN FPR Analysis
981 benign samples, accuracy 90.21% -> FPR ~10%
CIC-DDoS2019 class imbalance (15M attack vs 981 benign)
TreeLine as first-stage filter; flagged benign -> ARM re-evaluation
Cost-sensitive training in progress

## Slide 24
Backup C: Pipeline Resource Usage
Resource | Used | BF-2 Limit | Utilization
Pipes | 75 | >= 64 deep | Low
Entries | ~200 | ~256K | < 0.1%
Metadata registers | 5/5 | 5 | 100%

## Slide 25
Backup D: Entry Insertion Performance
~936K entries/sec
10K entries in 10.7 ms (batch insertion)
Model loading is not a bottleneck — TreeLine's 75-pipe RF loads in < 100 ms